High Performance Computing Seminar
Mesh Partitioning with METIS
Caroline Mendonça Costa

---
Introduction
- Parallel large-scale simulations of FE meshes require the distribution of the mesh to the processors
  - Same number of elements to each processor
    - Work load balance
  - Number of adjacent elements assigned to different processors is minimized
    - Minimization of the communication
- Graph partitioning can be used to satisfy these conditions

---
Overview of Metis
- Serial software package for
  - partitioning large irregular graphs
  - partitioning large meshes
  - computing fill-reducing orderings of sparse matrices
- Developed at the Department of Computer Science & Engineering at the University of Minnesota
- Freely distributed
- Can be downloaded at
  http://www.cs.umn.edu/~metis

---
The k-way Graph Partitioning
- Metis provides two methods to solve the k-way partitioning problem
  - Multilevel recursive bisection partitioning
  - Multilevel k-way partitioning

---
Multilevel Graph Bisection
- Coarsening phase
  - Vertices are collapsed together to form a series of smaller graphs
- Initial partitioning phase
  - Partitioning of the coarsest graph is computed
- Uncoarsening phase
  - Partitioning is projected onto the larger graphs
  - Partitioning is refined

---
Coarsening Phase
- A graph can be coarsened by finding a matching
  - Matching: set of edges without any loops
    - Vertices are collapsed together to form a multinode
  - Maximal matching: any edge in the graph that is not in the matching has at least one of its vertices matched

---
Coarsening Phase
- Random Matching (RM)
  - Vertex u is matched with one (randomly selected) of its adjacent vertices
- Heavy Edge Matching (HEM)
  - The total edge weight of the coarser graph is reduced by the weight of the matching
    - W(Ei+1) = W(Ei) – W(Mi) (i)
  - Smaller edge-weight > smaller edge-cut
  - HEM finds a maximal matching so that (i) decreases faster
  - Vertex u is matched with v, such that (u,v) is the heaviest edge

---
Coarsening Phase
- Modified Heavy Edge Matching (HEM*)
  - Graphs based on finite element meshes
    - Edges have the same weight
    - Similar to RM
  - HEM matches u with the vertex v that has the highest degree
    - Decreases the average degree of the coarser graph

---
Initial Partitioning Phase
- Spectral Bisection
  - Computes the eigenvector y corresponding to the second largest eigenvalue of the Laplacian matrix
    - y is called the Fiedler vector
    - r is chosen as the weighted median of the values of y
      - All vertices smaller than r are put in the first partition and other in the second partition
    - The Fiedler vector is computed using the Lanczos algorithm
      - Iterative algorithm: # of iterations depend on the desired accuracy
  - Not used in Metis!

---
Initial Partitioning Phase
- Graph Growing Algorithm (GGP)
  - Start from a vertex and grow a region around it in a breadth-first fashion until half of the vertices have been included
  - Sensitive to the choice of the first vertex
- Greedy Graph Growing Algorithm (GGGP)
  - For each vertex v defines a gain of inserting v in the growing region
    - The vertex with the largest decrease in the edge-cut is inserted first
  - Also sensitive to the choice of the initial vertex, but less than GGP
  - Performs better than GGP in terms of time and edge-cut

---
Uncoarsening Phase
- Assigns the vertices collapsed to v to the same partition that v belongs to
- At each uncoarsening level the partitioning is refined
  - Vertices are swapped between the partitions to improve the edge-cut
  - Kernighan-Lin Refinement

---
Uncoarsening Phase
- Kernighan-Lin refinement
  - Iteratively swaps vertices among partitions of a bisection to reduce the edge-cut
    - Uses two priority queues, one for each partition, according to their gains
    - Iteratively moves vertices at the top of the priority queues
    - Stops when all vertices were moved
    - Calculates where the smallest edge-cut was achieved and moves back the vertices that were moved after this point

---
Multilevel k-way Graph Partitioning

---
Initial Partitioning Phase
- One way to produce the initial k-way partitioning is to keep coarsening the graph until it has k vertices left
  - The reduction in the size of the graph becomes small after a few coarsening steps
  - The weights of the vertices are likely to be quite different, making the initial partition unbalanced
- In Metis the initial k-way partitioning is computed using the multilevel bisection algorithm
  - Produces good initial partitioning in a small time as long as the size of the original graph is sufficiently larger than k

---
Uncoarsening Phase
- Extension of KL refinement for the case of k-way refinement uses k(k-1) priority queues
  - One queue for each type of movement
  - Only suited for small values of k
  - Sequential nature
- Using priority queues allow movement of several vertices sequentially
  - In a multilevel context the priority queues become less important
    - Nodes of coarsest graph are multinodes
    - Nodes with the highest gains are moved anyway

---
Uncoarsening Phase
- Greedy Refinement
  - Vertices are moved only if they lead to positive gain
  - GR visits the boundary vertices at each iteration in random order
    - Moves a vertex v to a partition the leads to the largest reduction in the edge-cut (while preserving the balance conditions) or to an improvement in the balance
  - Converges after a small number of iterations
    - When combined with HEM or HEM* converges after 4-8 iterations
  - Parallel nature
    - Communication volume is smaller than in KL refinement

---
MRBP versus MkP
Coarsening
phase
Uncoarsening
phase
Initial
partitioning
MRBP
MkP
Coarsening
phase
Uncoarsening
phase
Initial
partitioning
MRBP

---
Some results...
- Mesh with 4,000,000 elements
- MkP (O(|E|)) is much faster than MRBP (O|E| log(k)))
- Partitioning with MkP is slightly better

---
Final Considerations
- MkP is significantly faster and produces comparable or better partitions than MRBP
  - MkP is O(|E|) and MRBP is O(|E| log(k))
    - As MRBP is applied to a much smaller graph the total execution time depends mainly on the number of edges
  - HEM* produces a very good smaller replica of the original graph
    - MkP produces a good partitioning based on the coarse graph
  - Simple refinement as GR improves the partitioning after a few iterations